## Slide 1: DIP Seminar Week 2
최성욱

## Slide 2: Contents
Make up for last week
Morphological Processing of Binary Image
Thresholding

## Slide 3: Make up for last week
Notation
Originality
“1”’s meaning of Affine matrix
HSI model of RGB full color cube

## Slide 4: Make up for last week – Affine Matrix
Using an augmented matrix and an augmented vector, it is possible to represent both the translation and the linear map using a single matrix multiplication.
By representing a 2-vector (x, y) as a 3-vector (x, y, 1), translation can be expressed with matrix multiplication.
The matrix form,
can be expressed as,
: original coordinate
: transformed coordinates : translation coefficients

## Slide 5: Make up for last week – HSI Model
RGB full color cube
Hue
Saturation
Intensity
HSI Model

## Slide 6: Morphological Processing of Binary Image
Erosion & Dilation
Opening & Closing
Some Morphological algorithm.
Morphological Reconstruction

## Slide 7: Morphology
A tool for extracting image components that are useful in the representation and description of region shape, such as boundaries, skeletons, and the convex hull.
A tool for extracting “meaning” from an image.
The language of mathematical morphology is set theory.

## Slide 8: The definitions of and
: The reflection of a set B
The translation of a set B by point z = (z1, z2)

## Slide 9: Structuring Elements(SEs)
Small sets or subimages used to probe an image under study for properties of interest.
Examples of structuring elements
Structuring elements converted to rectangular arrays.
Shaded square denotes a member of the SE.
The dot denotes the centers of the SE

## Slide 10: Erosion
The erosion of A by B, denoted, A ⊖ B, is defined as
or
Erosion shrinks the components of an image.
or
Erosion of A by B, shown shaded.
A is the set (image object).
B is a structuring element.

## Slide 11: Erosion
Original Image
Image eroded using SE of size 13x13
Using SE of size 15x15
Using SE of size 45x45
The elements of the SEs were all 255s.
a b
c d

## Slide 12: Erosion
Width : 13 pixels
Width : 1 pixel
Image eroded using SE of size 13x13
Original image

## Slide 13: Dilation
The dilation of A by B denoted A ⊕ B, is defined as
or
Dilation expands the components of an image
A is the set (image object).
B is a structuring element.
Dilation of A by B, shown shaded.

## Slide 14: Dilation
SEs:
⊕
⊕
A
A
A

## Slide 15: Duality
Erosion and dilation are duals of each other with respect to set complementation and reflection. That is,
and
Dilation
A
Ac

## Slide 16: Opening
The opening of set A by structuring element B, denoted A ◦ B , is defined as
Opening generally smoothes the contour of an object, breaks narrow isthmuses, and eliminates thin protrusions.
The opening of A by B
A is not shaded for clarity
:The union of all the sets inside the braces

## Slide 17: Closing
The closing of set A by structuring element B, denoted A • B, is defined as
Closing also tends to smooth sections of contours but, as opposed to opening, it generally fuses narrow breaks and long thin gulfs, eliminates small holes, and fills gaps in the contour.
The closing of A by B
A is not shaded for clarity

## Slide 18
Morphological opening and closing.
The SE is the small circle in the left image.
Outward pointing corners were rounded by opening.
Whereas inward pointing corners were rounded by closing.

## Slide 19: Opening and Closing
B: Structuring element
A
A ⊖ B
(A⊖B)⊕B
A ◦ B
(A ◦ B) ⊕ B
[(A ◦ B) ⊕ B] ⊖ B
(A ◦ B) • B

## Slide 20: Boundary Extraction
The boundary of a set A, denoted by (A ), defined as
where B is a suitable structuring element.

## Slide 21: Boundary Extraction
(a) Original image
(b) - (d) Results of boundary extractions using SEs of size 3x3, 5x5, 11x11 respectively. The elements of the SEs were all 255s.
(d)
(b)
(c)
(a)

## Slide 22: Hole Filling
The following procedure fills all the holes
X0 : An array of 0s, except at the locations in corresponding to the given point in each hole, which we set to 1.
The algorithm terminates if Xk = Xk-1. Then the set Xk contains all the filled holes.

## Slide 23: Hole Filling
Original Image
One hole filled
Two holes filled
All holes filled
a b
c d

## Slide 24: Hole Filling
Origianl Image
X0
X6
(46,64)
X26, Fully Filled Hole

## Slide 25: Morphological Reconstruction
Morphological reconstruction is a powerful morphological transformation.
Morphological reconstruction involves two images and a structuring element.
One image, the marker, contains the starting points for the transformation.
The other image, the mask, constrains the transformation.

## Slide 26: Geodesic dilation
The geodesic dilation of size 1 denoted by , is defined as ,
The geodesic dilation of size n is defined as,
F: The marker image
G: The mask image

## Slide 27: Morphological reconstruction by dilation
Morphological reconstruction by dilation denoted , is defined as
F: The marker image, G: The mask image.
F, B, and are from previous slide

## Slide 28: Opening by reconstruction
The opening by reconstruction of size n is defined as
F: An image, B: The SE of the erosion, (F ⊖ nB): n erosions of F by B.
erosion
opening
opening by reconstruction
The SE of erosion were 51x1 size and all elements were 255s

## Slide 29: Automatic hole filling
Let I(x, y) denote a binary image and suppose that we form a marker image F, that is
Then, is a binary image equal to with all holes filled.
SE
Original Image
Hole Filled Image

## Slide 30: Automatic hole filling
, Marker Image
Dn : Geodesic dilation of size n
: Reconstruction by dilation
, Mask Image

## Slide 31: Border clearing
Let denote a binary image and suppose that we form a marker image F, that is
Then, is a border image of and is border cleaned image.
Original image
Border of original image
Border cleaned image

## Slide 32: Thresholding
Histogram
Basic Global Thresholding
Otsu’s Thresholding
Multiple Thresholds: Especially for three thresholds
Variable Thresholding: Image partitioning & Local Threshold

## Slide 33: Histogram
The histogram of a digital image with intensity levels in the range [0, L - 1] is a discrete function
A normalized histogram is given by
.
: the kth intensity value
: the number of pixels with intensity
M : row dimension of the image
N : column dimension of the image

## Slide 35: Thresholding
Techniques for partitioning images directly into regions based on intensity values and/or properties of these values.
Let f(x,y) denote the original image. Then the segmented image, g(x,y) is given by
When T is a constant applicable over an entire image, the process given in this equation is referred to as global thresholding.
When the value of T changes over an image, we use the term variable thresholding.

## Slide 36: Basic Global Thresholding
Select an initial estimate for the global threshold, T
Segment the image using T. This will produce two groups of pixels: G1 consisting of all pixels with intensity values > T and G2 consisting of pixels with values ≤ T.
Compute the average (mean) intensity values m1, m2 for the pixels in G1, G2 respectively.
Compute a new threshold value: T = (m1 + m2)
Repeat Steps 2 through 4 until the difference between values of T in successive iterations is smaller than a predefined parameter T.
Using T0 = 127, T = 1,
get Tfinal = 125
Histogram of original image

## Slide 37: Otsu’s Optimum Global Thresholding
This threshold is determined by minimizing intra-class intensity variance, or equivalently, by maximizing inter-class variance (between-class variance), a well-known measure used in statistical discriminant analysis.
The between-class variance, is defined as
Then, the optimum threshold is the value, k*, that maximizes :

## Slide 38
Basic Global
Algorithm
Otsu’s
Algorithm
kth = 169
kth = 181
Normalized Histogram
kth :The intensity value of threshold

## Slide 39: Using Image Smoothing to Improve Global Thresholding
Otsu’s
Algorithm
Otsu’s
Algorithm
5x5 Box Filtering
Histogram of original image
Histogram of smoothed image

## Slide 40: Multiple Thresholds
The thresholding method can be extended to an arbitrary number of thresholds.
In the case of K classes, C1, C2, ... , CK, the between-class variance generalizes to the expression
Then the threshold values, are values that maximize

## Slide 41: Multiple Thresholds for three classes(Dual thresholding)
The between-class variance is given by:
The two optimum threshold values, and are such that
Then the thresholded image is then given by

## Slide 42: Multiple Thresholds
(a) Image of iceberg
(b) Histogram of (a)
(c) Thresholded Image

## Slide 43: Image partitioning
One of the simplest approaches to variable thresholding is to subdivide an image into nonoverlapping rectangles.
subdivide
Otsu’s Algorithm
Otsu’s algorithm
to each subimages
Histogram of the original image

## Slide 44: Image partitioning
Histograms of each subimage
Image subdivided into 6 subimages

## Slide 45: Local thresholding using the standard deviation and mean
Let denotes the standard deviation of the set of pixels contained in a neighborhood, and denotes the global mean of the input image, .
Then the following are common forms of variable, local thresholds:
,
where a and b is nonnegative constants.
The segmented image, is computed as

## Slide 46: Local thresholding
Original image.
Image segmented using the dual thresholding.
Image of local standard deviations.
Result obtained using local thresholding. The value of a = 30, and b = 1.5 .
a b
c d

## Slide 47: Local thresholding
Text image corrupted by spot shading.
Result of Otsu’s global thresholding.
Result of local thresholding. The value of a = 1, and b = 0.5 .
The value of a = 5, and b = 0.5
a b
c d

## Slide 48: Local thresholding
Text image corrupted by spot shading.
Result of Otsu’s global thresholding.
Result of local thresholding. The value of a = 1, and b = 0.5 .
The value of a = 5, and b = 0.5
a b
c d

## Slide 49: Optimization
Morphological image processing, especially morphological reconstruction takes a lot of time to perform.
I found that accessing time for element of “Mat” is a little bit long. So I change the algorithm of geodesic dilation.

## Slide 50: Reference
Rafael C. Gonzalez, Richard E. Woods - Digital Image Processing (2008, Prentice Hall)